## Slide 1: Measuring the Fraction of CO2 in Air with Fourier Transform Infrared Spectroscopy
Esther Lin | ENPH 352

## Slide 2: Objectives
To measure the fraction of CO2 in air
To measure and understand the absorption spectra of N2, CO2 and air (aggregation of atmospheric gases)

## Slide 3: Theory
In the mid-infrared region of the electromagnetic spectrum, molecules absorb light through the interaction between the photons and the vibrating electric dipoles of the molecule.
In FTIR, a beam carrying many frequencies irradiates a sample. We measure how much of that beam is absorbed and transmitted by the sample.
With the transmission and absorbance spectra, we can identify the molecules in the sample.
http://brussels-scientific.com/?p=5975
Vibrational modes of molecules

## Slide 4: General Setup
The FTIR is based on the Michelson interferometer. A multimode laser transmits light on the beamsplitter, which splits the light into two beams. The first beam hits the stationary mirror and transmits to the detector through the gas cell. The second beam travels to the scanning mirror. By translating the scanning mirror, different wavelengths in the beam are selected to pass through the gas cell. The detector records the interaction of the beams with the molecules (interferogram) in the gas cell and sends the information to a computer for Fourier Transform analysis.
Notes: Big paragraph. List components bullet points.

## Slide 5: Method: Data Collection
Interferogram captured with no gas cell, and the FTIR flushed with N2. We proceed to capture interferograms where the gas cell is in place, flushed with N2, CO2, and air, all with FTIR flushed with N2.
Notes: Caption interferogram. Take out fluff. Do caption style.

## Slide 6: Method: Data Analysis
Normalization spectra, collected with a flushed N2 cell. Mertz correction was applied to smooth noise from from the Fourier Transform. The intensity of this spectra is used to calculate the transmittance and absorbance spectrums for N2, CO2 and air with the Beer-Lambert Law:
Transmission: Absorbance:
Notes: Less procedural, more general.

## Slide 7: Method: Mertz Correction
Comparison of spectra with and without Mertz correction. The Mertz correction method modulates the spectra with a triangular signal, to smooth out ringing with taking the Fourier transform of the interferogram. The spectrum with the Mertz correction is smoother and less noisy.

## Slide 8: Results: Spectrums of CO2
(a) Transmission spectra of CO2. (b) Absorption spectra of CO2. We see a strong peak around 2350 cm-1, which is where CO2 absorbs. Hence, the FTIR has identified the CO2 in our gas cell of CO2.
(a)
(b)
CO2
H2O

## Slide 9: Results: Spectrums of Air
(a) Transmission spectra of air. (b) Absorption spectra of air. We see a weak peak around 2350 cm-1, which is where CO2 absorbs. Hence, the FTIR has identified the CO2 in our gas cell of air.
(a)
(b)
CO2
H2O

## Slide 10: Results: Spectrums of N2 (control)
(a) Transmission spectra of N2. (b) Absorption spectra of N2. We that N2 does not absorb at 2350 cm-1. This spectrum is very similar to that of air, since air is ~ 75% N2.
(a)
(b)
CO2
H2O

## Slide 11: Results: Summary
Molecule | Measured Wavenumber [cm-1] | Expected Wavenumber [cm-1]
CO2 | 2352 ± 22 | 2362
Molecule | Measured Fraction [%] | Expected Fraction [%]
CO2 in air | 8 ± 1 | 0.04

## Slide 12: Conclusions
FTIR is a useful tool for the identification of molecules in gas samples
Lineshape characteristics (width, tail) in FTIR spectrums can be used to infer the type of molecular movements and interactions in the sample
Measurements of gas cells are limited by the thoroughness of flushing